DSD Assignment

Full-Adder

Description :-
- A full adder is a one-bit adder that adds three one-bit numbers, often written as A, B, and Cin
- A and B are the operands, and Cin is a bit carried in from the previous less-significant stage.
- Output carry and sum typically represented by the signals Cout and S.

Full adder Circuit Diagram

Truth Table :-

a	b	cin(c)	sum	cout(c1)
0	0	0	0	0
0	0	1	1	0
0	1	0	1	0
0	1	1	0	1
1	0	0	1	0
1	0	1	0	1
1	1	0	0	1
1	1	1	1	1

Waveform:-

Code:-
Gate-Level

module fulladder (sum, c_out, in0, in1, c_in); / output sum, c_out; / input in0, in1, c_in; / wire xor_1,xor_2,and_1,and_2,or_1; / //outputs of each gate / xor x1(xor_1,in0,in1); / and a1(and_1,xor_1,c_in); / xor x2(sum,xor_1,c_in); / and a2(and_2,in0,in1); / or o1(c_out,and_2,and_1); / endmodule

Dataflow Level

module fulladder (sum,c1,a,b,c); / output sum,c1; / input a,b,c; / assign sum=() / assign c1=(b&&c); / endmodule

Behavioural Level
module fulladder (sum, c_out, in0, in1, c_in); / output sum, c_out; / input in0, in1, c_in; / assign { c_out, sum } = in0 + in1 + c_in; / endmodule

Testbench

`timescale 1ns/100ps / `include "fulladder.v" / module Top; / wire sum,c1; / reg a,b,c; / fulladder fu1(sum,c1,a,b,c); / initial / begin / $dumpfile("fulladder.vcd"); / $dumpvars; / $monitor($time,"a=%b, b=%b , c=%b ,sum=%b, carry=%b\n",a,b,c,sum,c1); / a=0;b=0;c=0; / #5 a=0;b=0;c=1; / #5 a=0;b=1;c=0; / #5 a=0;b=1;c=1; / #5 a=1;b=0;c=0; / #5 a=1;b=0;c=1; / #5 a=1;b=1;c=0; / #5 a=1;b=1;c=1; / #5 a=0;b=0;c=0; / #5; / end / endmodule

4-to-1 Multiplexer

Description :-

- A multiplexer, abbreviated mux, is a device that has multiple inputs and one output.
- A multiplexer of 4 inputs has 2 select lines, which are used to select which input line to send to the output

Circuit Diagram of 4-to-1 multiplexer

Truth Table:

Select[1]	Select[0]	Q(output)
0	0	0
0	1	1
1	0	2
1	1	3

Waveform:

Code:

Gate Level
module fulladder (sum, c_out, in0, in1, c_in); / output sum, c_out; / input in0, in1, c_in; / wire xor_1,xor_2,and_1,and_2,or_1; / //outputs of each gate / xor x1(xor_1,in0,in1); / and a1(and_1,xor_1,c_in); / xor x2(sum,xor_1,c_in); / and a2(and_2,in0,in1); / or o1(c_out,and_2,and_1); / endmodule

Dataflow

module mux( select, d, q ); / input[1:0] select; / input[3:0] d; / output q; / assign q=(d[0]&&!select[0]&&!select[1]) / ||(d[1]&&select[0]&&!select[1]) / ||(d[2]&&!select[0]&&select[1]) / ||(d[3]&&select[0]&&select[1]); / endmodule

Behavioural

module mux( select, d, q ); / input[1:0] select; / input[3:0] d; / output q; / wire q; / wire[1:0] select; / wire[3:0] d; / assign q = d[select]; / endmodule

Testbench

`timescale 1ns/100ps / `include "mux.v" / module Top; / reg[3:0] in; / reg[1:0] sel; / wire q; / mux mux1(sel,in,q); / initial / begin / $dumpfile("mux.vcd"); / $dumpvars; / $monitor($time,"sel=%b, d=%b, q=%b\n",sel,in,q); / sel=2'b01;in=4'b1000; / #5 sel=2'b00;in=4'b1010; / #5 sel=2'b11;in=4'b1000; / #5 sel=2'b10;in=4'b1011; / #5 sel=2'b01;in=4'b1111; / #5 sel=2'b10;in=4'b0010; / #5 sel=2'b11;in=4'b0100; / #5 sel=2'b00;in=4'b1110; / #5 sel=2'b01;in=4'b0011; / #5; / end / endmodule

Xor Gate

Description :-

- A multiplexer, abbreviated mux, is a device that has multiple inputs and one output.
- A multiplexer of 4 inputs has 2 select lines, which are used to select which input line to send to the output

Diagram of Xor Gate

Truth Table:

a	b	out
0	0	0
0	1	1
1	0	1
1	1	0

Waveform:

Code
Gate Level
module Xor(out,a,b); / output out; / input a,b; / wire and_1,and_2,or_1; / and a1(and_1,!a,b); / and a2(and_2,a,!b); / or o1(or_1,and_1,and_2); / assign out =or_1 ; / endmodule

Dataflow
module Xor(out,a,b); / output out; / input a,b; / assign out =(!a&b)||(a&!b); / endmodule

Behavioural
module Xor(out,a,b); / output out; / input a,b; / reg out; / always @(a or b) / begin / if(a==b) / out = 0; / else / out =1; / end / endmodule

Testbench
`timescale 1ns/100ps / `include "xor.v" / module Top; / reg a,b; / Xor xo(out,a,b); / initial / begin / $dumpfile("xor.vcd"); / $dumpvars; / $monitor($time,"a=%b, b=%b , out=%b\n",a,b,out); / a=0;b=0; / #5 a=0;b=1; / #5 a=0;b=1; / #5 a=1;b=0; / #5 a=1;b=0; / #5 a=1;b=1; / #5 a=1;b=1; / #5 a=0;b=0; / #5; / end / endmodule